## Slide 1: Tips and Suggestions for Hardware Implementation Study of EE464
İlker Şahin
Apr. 2018

## Slide 2: Outline
What to look for on the internet
  Some general advices
  Proposed simplifications
  Hardware implementation steps
  Advanced issues and further reading
FEEL FREE TO ASK QUESTIONS

## Slide 3: What to look for on the internet
Two main sources:
  Application notes
    Usually offered by companies
    For you at this stage, better than IEEE articles
  Reference designs available on the internet
    Consider only TI to avoid further complication

## Slide 4: Some general advices
  To avoid ambiguity: DCM is OK for your converters
  You need further reading on TR design.
  Controller advice: UC384X
  Buying TR material: Ask and note these two parameters:
    Size & Shape: ETD24
    Core material: N87
  Stacking is a possibility, custom coil-former (karkas), etc…

## Slide 5: Simplification #1
  You are allowed to use an external power supply for your controller.
  This eliminates:
  Many components of a practical design
  The auxilliary transformer winding

## Slide 6: Simplification #2
  Forget about isolation (at the initial phases)
  Note that:
  Industry standard is TL431 + Optocoupler (for low-cost SMPS)
  Isolation amplifiers, hall sensors, etc..

## Slide 7: Tip: Explore your controller IC
  How does your IC work?
  Have you read about ‘Current Mode Control’ ?
  Try finding application notes that utilize the same IC

## Slide 8: Tips: On the control loop…
  Try an existing design, you may select slightly larger R and C values
  Try to learn the concept but do not get lost in control
  Initially, go with the SS performance, do not stress on dynamic performance
  Spikes at current sensing will most probably be a problem

## Slide 9: Steps for hardware implementation -1
  Converter design and simulation
  Design and create the transformer:
    Initial overdesign is normal
    Test your transformer: resistances, inductances, drive with signal generator, try with lower voltage, etc..
  Solder main parts
  Drive open loop: provide a fixed duty cycle PWM without a control loop just to test converter performance

## Slide 10: Steps for hardware implementation -2
  Test converter performance (first low then nominal voltage)
    Are feedback signals ‘clean’?
    Is the switch stress as expected?
    Examine spikes, noisy signals, audible noise, heating
  Test your control circuitry
  Combine controller + converter
  Cancel simplifications and evolve into a practical design

## Slide 11: EMI & EMC
  Proper wiring and proper geometry for the components
  Magnetic elements may require extra spacing
  Stray inductance is (for most of the time) your enemy
  Bypass capacitor is (for most of the time) your friend
  Learn proper grounding techniques
  Learn the value of isolation and the means to obtain it
  Search for: ferrite bead (or choke), common mode filter
  If dynamic performance is not of primariy concern, go with LPF

## Slide 12: Final tips
  Current mode control (inevitable for complex systems)
    Average current control
    Peak current control
  Advanced issues related with CMC: sub-harmonic oscillation, slope compensation (Google them)
  ‘Switching Power Supplies A – Z’ by Sanjaya Maniktala, 2nd Edition